TEMPEST sniffing monitor
KAIR neural network to denoise image
Ondrej Mikle • ondrej.mikle@gmail.com • 16.4.2025

---
Electromagnetic emanations
all time-varying voltage and current interfaces emit electromagnetic waves
  - chips, cables, all PCB traces act as transmitter antennas
  - signal can be -50 dBm or lower (less than 0.01 μW), even -130 dBm workable
  - current off-the-shelf SDRs can capture it, generally have >=90 dB dynamic range
  - e.g. BladeRF, USRP B210, H-field probe

---
Sample EM trace of ARM chip

---
HDMI emanation & interference

---
VGA/HDMI/DisplayPort/USB-C
- VGA is trivial to sniff, analog
- HDMI & LVDS (LVDS is used in notebooks) have differential signalling, but still sniffeable
- DisplayPort is differential signalling, but with some PRNG to not make it so easy, can be partially filtered out, but with loss
- USB-C is network that encapsulates DisplayPort – hard to catch pixelclock

---
Front/back porch/pixelclock (1)

---
Front/back porch/pixelclock (2)
Resolution alone does not give horizontal/vertical or pixelclock timings, depends
on display and other things

---
Front/back porch/pixelclock (3)
- pixelclock in MHz gives you timing for whole image, all these values neeed to be correct
- horizontal and vertical pixels are needed to make sense of the signal
- I found 5th harmonic frequency of pixelclock works best for me
  - e.g. pixelclock of 148.5 MHz has 3rd harmonic 445.5 MHz and 5th 742.5 MHz

---
Antennas & filters
- better antennas and filters result in better images, i.e. better specify what is sniffed
- I used generic omnidirectional antennas, but log-periodic can be better
log-periodic antenna
omnidirectional antennas

---
Software stacks
- kinda all
  - Java + native libs
  - C++
  - python + C/C++ native libs multiprocessing

---
First results, monitor original
made a mistake to enlarge image via interpolation, thus losing edges

---
First results, TEMPEST image

---
High-contrast sharp image

---
Best you can hope with just SDR

---
What next?
- enhance image somehow
- there is KAIR image restoration library you can use to train on some images
- training on web pages, PDFs and text is generally useful for attacker, as he wants to see some secret documents

---
Thanks
Ondrej Mikle • ondrej.mikle@gmail.com